SECTION 10 2800

TOILET ACCESSORIES

- - GENERAL

  - SUMMARY

    - Provide toilet accessories with attachment hardware and rough-in frames as required for complete, operational installation.

    - Section Includes:

      - Toilet Room, Lavatory, and Shower Accessories.

      - Mirrors

      - Hospital and Medical Service Accessories.

      - Security/Detention Accessories.

      - Automatic Hand Dryers.

    - Related Requirements

      - See drawings for wall/partition types and additional mounting requirements.

      - Coordinate electrical supply and connections.

  - REFERENCES

[Revise to comply with state and local codes for specific project]

    - ADAAG:  Americans with Disabilities Act Accessibility Guidelines.

    - ANSI A117:  Specifications for Making Buildings and Facilities Accessible to and Usable by Physically Handicapped People.

    - IBC – Chapter11, Accessibility.

    - Fair Housing Amendments Act of 1988, Accessibility Guidelines, Federal Register Volume 56, Number 44.

    - State Requirements (i.e., California Building Code Chapter 11)

  - COORDINATION

    - Coordinate locations, dimensions, and other pertinent details with installation of backing, blocking, and electrical connections.

  - LEED® REQUIREMENTS

    - MR Credit 4.1 - Recycled Content (post-consumer).

    - MR Credit 4.2 - Recycled Content (post-industrial).

  - SUBMITTALS

    - Submit under provisions of Section 01 3000.

    - Product Data:  Manufacturer's product data for products specified, indicating selected options and accessories.

    - Shop Drawings:

      - Plans:  Locate each specified unit in project.

      - Elevations:  Indicate mounting height of each product.

      - Details:  Indicate anchoring and fastening details, required locations and types of anchors and reinforcement, and materials required for installation of specified products.

    - Verification Samples:  One sample chips of each specified color and finish.

    - Manufacturer's printed installation instructions for each specified product.

    - Closeout Submittals:  Warranty, issued and executed by manufacturer, and countersigned by Contractor.

      - One set of special adjusting or installation tools unique to the products furnished under this section.

      - Keys to accessories furnished under this section.

  - DELIVERY, STORAGE, AND HANDLING

    - Ship products in manufacturer's standard protective packaging with removable protective coating on exposed surfaces.

    - Storage and Protection:  Store products in manufacturer's protective packaging in a dry, climate controlled environment until installation.

  - WARRANTY

    - Provide manufacturer's standard warranty against defects in materials and fabrication.

    - Provide manufacturer's 15-year warranty against silver spoilage of mirrors.

- - PRODUCTS

  - MANUFACTURERS

    - ASI-American Specialties, Inc.; 441 Saw Mill River Road, Yonkers NY 10701-4913; Tel:  (914) 476-9000, Fax: (914) 476-0688.  www.americanspecialties.com

    - Furnish products from a single manufacturer.

    - Standard of Quality:  Drawings and specifications are based on proprietary literature from ASI.  Other manufacturers shall comply with the minimum levels of material and detailing indicated on the Drawings and as specified.

  - ROVAL COLLECTION

    - Basic Construction Requirements:

      - Doors:  Curved design, one piece stainless steel.

      - Cabinets:  Stainless steel, trimless; joints welded, sight-exposed welds finished to match sheet finish.  Full access back panels.

      - Hinges:  Concealed, multi-staked stainless steel piano hinge, full length of cabinet.

      - Locks:  2 flush, rimless tumbler locks, keyed alike other toilet accessory locks, with one key for each lock.

      - Exposed Finish:  No.4 satin finish, unless noted otherwise.

  - TRADITIONAL COLLECTION

    - Basic Construction Requirements:

      - Doors:  Type 304, 22-gage stainless steel, double pan construction, with 1/4-inch thick structural fiberboard core.

      - Cabinets:  Type 304, 22-gage stainless steel, formed perimeter trim with 1/4-inch return to wall four sides; joints welded, sight-exposed welds finished to match sheet finish.

      - Hinges:  Stainless steel piano hinge, 3/16-inch diameter barrel, full length of cabinet; hinge leaves spot-welded to door and cabinet body.

      - Locks:  Tumbler locks, keyed alike other toilet accessory locks, with one key for each lock.

      - Cabinet and Door Finish:  No.4 satin finish.

  - SIMPLICITY COLLECTION

    - Basic Construction Requirements:

      - Doors:  Type 304, 18-gage stainless steel, formed 1/2-inch return to wall.

      - Cabinets:  Type 304, 20-gage stainless steel, formed 1-inch wide flat perimeter trim four sides; joints welded, sight-exposed welds finished to match sheet finish.

      - Hinges:  Stainless steel piano hinge, 3/16-inch diameter barrel, full length of cabinet; hinge leaves spot-welded to door and cabinet body.

      - Locks:  Tumbler locks, keyed alike other toilet accessory locks, with one key for each lock.

      - Cabinet and Door Finish:  No.4 satin finish.

  - PROFILE COLLECTION

    - Basic Construction Requirements:

      - Doors:  Type 304, 16-gage stainless steel, formed 15/16-inch return to wall, with vertical edges eased at 3/4-inch radius; welded corners.

      - Cabinets:  Type 304, 20-gage stainless steel, formed 1-inch wide flat perimeter trim four sides; joints welded, sight-exposed welds finished to match sheet finish.

      - Hinges:  Stainless steel piano hinge, 3/16-inch diameter barrel, full length of cabinet; hinge leaves spot-welded to door and cabinet body.

      - Locks:  Flat rimless tumbler locks, keyed alike other toilet accessory locks, with one key for each lock.

      - Cabinet and Door Finish:  No.4 satin finish.

  - MIRRORS

SPECIFIER NOTE:  Select mirror assembly and edit materials accordingly.

    - Mirror:  Model ______.

      - Frame:  [Angle – 0600]  [Channel - 0620]. Model ______.

      - Mirror:  [Plate glass - A]  [Tempered glass - B]  [Stainless Steel - C]  [Polycarbonate - D]  [Acrylic - E]  [Laminated glass - L]. Model ______.

      - Shelf:  [Angle – 0605]  [Channel - 0625].

      - Size:  As indicated on drawings.

      - Finish:  No.4 satin stainless steel.

    - Roval Stainless Steel Mirror:  Model 20650.

      - Frame:  18-gage stainless steel.

      - Mirror:  1/4-inch float glass [tempered glass 20650-B].

      - Size:  As indicated on drawings.

      - Finish:  No.4 satin stainless steel.

      - Shelf:  Model 20655, curved edge shelf.

  - GRAB BARS

    - Grab Bars:  Comply with ASTM F446 from ASTM A554 stainless steel tubing, 18-gage, Type 304; formed [1-1/4 inch] [1-1/2 inch] radius return to wall at each end; heliarc-welded to minimum 11-gage stainless steel flange.

SPECIFIER NOTE:  For grab bars, the Series defines whether it has concealed or exposed mounting and the diameter of the tube.

    - Grab Bars:  Series ______.

      - Peened finish. [P]

      - Sizes and configurations:  As indicated on drawings.

      - Sizes and configurations:  As indicated in Schedule at end of section.

    - Concealed Mounting Flanges-Set Screws: [3100 Series – 1 ¼”] [3200 Series – 1 ½”]   Stainless steel, 3-inch diameter by 1/2-inch deep, with 13-gage steel tenon plate for concealed attachment, using three set screws.

    - Concealed Mounting Flanges-Snap-on:  [3700 Series – 1 ¼”] [3800 Series – 1 ½”] Stainless steel cover, 22-gage, 3-inch diameter by 1/2-inch deep, snaps over 1/8-inch thick stainless steel mounting flange.

    - Exposed Mounting Flange:  [3400 Series – 1 ¼”] [3500 Series – 1 ½”] Stainless steel, 1/8-inch thick, and 3-inch diameter, with 3-countersunk screw holes.

      - Finish:  [Grey] or [White].

  - HANDS FREE ACCESSORIES

SPECIFIER NOTE:  Indicate whether hands free units are battery or AC powered.

    - Soap Dispensers.

      - Model 0360:  Stainless steel, #4 satin finish, proximity sensor, battery operated.

      - Model 0362:  Stainless steel, #4 satin finish, proximity sensor, battery operated.  For higher viscosity soaps

      - Roval Model 20333:  Deck-mounted, stainless steel, polished finish, proximity sensor, battery operated.

      - Roval Model 20363:  Surface mounted, stainless steel, satin finish.

      - Roval Model 20364:  Stainless steel, satin finish, proximity sensor, battery operated.

      - Roval Model 20365:  Automatic Foam Soap Dispenser, stainless steel, satin finish.

    - Towel Dispensers.

      - Model 046921A:  Automatic roll towel dispenser and 14-gallon waste receptacle.  Proximity sensing no-touch.  Recessed unit.

      - Model 046924A:  Automatic roll towel dispenser and 14-gallon waste receptacle.  Proximity sensing no-touch.  Surface mount unit.

      - Model 94696A:  Automatic roll towel dispenser and 10-gallon waste receptacle.  Proximity sensing no-touch.  Recessed unit.

      - Model 04692A:  Automatic roll towel dispenser and 18-gallon waste receptacle.  Proximity sensing no-touch unit.  Recessed unit.

      - Model 045224A:  Automatic roll towel.  Proximity sensing no-touch unit.  Recessed unit.

      - Model 04523A:  Automatic roll towel dispenser.  Proximity sensing no-touch unit.  Recessed unit.

      - Model 8522A:  Automatic roll towel dispenser.  Proximity sensing no-touch unit.  Surface mounted unit.

      - Model 64696A:  Automatic roll towel dispenser and 8.6-gallon waste receptacle.  Proximity sensing no-touch.  Recessed unit.

      - Roval Model 204523A:  Automatic roll towel dispenser.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  Battery operated.

      - Roval Model 204523A:  Automatic roll towel dispenser.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  110-240VAC operation.

      - Roval Model 204692A:  Automatic roll towel dispenser and 17.75 gallon waster receptacle.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  Battery operated.

      - Roval Model 204692AC:  Automatic roll towel dispenser and 17.75 gallon waster receptacle.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  110-240VAC operation.

      - Roval Model 2046921A:  Automatic roll towel dispenser and 13.5 gallon waster receptacle.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  Battery operated.

      - Roval Model 2046921AC:  Automatic roll towel dispenser and 13.5 gallon waster receptacle.  Proximity sensing no touch.  Surface mount, semi-recessed, and recessed types.  110-240VAC operation.

  - AUTOMATIC HAND DRYERS

    - Turbo-Dri.  Model 0197-1, 120VAC. [0197-2, 240VAC]

      - Cover fabricated of heavy-duty, one piece formed stainless steel 1/16" thick, exposed surfaces satin or bright or heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with white porcelain enamel.

      - Motor:  3/8 - 1 HP, brush type, dual ball bearing, 7000-18000 RPM.

      - Infrared sensor.

      - GreenSpec® listed.

      - Finish:  [Steel housing with Porcelain enamel] or [Stainless steel, {Bright} {Satin} finish].

      - Turbo-Dri optional semi-recessed mounting kit, Model 0119 – ADAAG Compliant.

        - Less than 4-inch protrusion from mounting surface.

    - Roval Steel Cover, Model 0185 [Universal Voltage]

      - Cover fabricated of heavy-duty, one piece formed stainless steel 1/16" thick, exposed surfaces satin or bright or heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with white porcelain enamel.

      - Motor1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  [Steel housing with Porcelain enamel] or [Stainless steel, {Bright} {Satin} finish].

    - Roval Cast Iron Cover, Model 0195  [Universal Voltage]

      - Cover fabricated of heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with porcelain enamel.

      - Motor 1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  Steel housing with Porcelain enamel.

        - Color as selected.

    - Roval Recessed Steel Cover, Model 20199 [120-240 VAC]

      - Cover fabricated of heavy-duty, one piece formed 18-gage stainless steel exposed surfaces.

      - Motor 0.69 HP, brush type, dual ball bearing, 29000 RPM.

      - Infrared sensor.

      - Finish:  Stainless steel, Satin finish.

    - Model 0133  [Universal Voltage]

      - Cover fabricated of heavy-duty, 14-gage seamless stainless steel cover, exposed surfaces satin finish.

      - Motor:  1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  Stainless steel, Satin finish.

    - Model 64673, Three-in-one unit recessed combination paper towel dispenser, automatic hand dryer and waste receptacle.

      - Three-in-one unit combines towel dispenser, automatic hand dryer and a four gallon stainless steel waste receptacle in one unit.

    - Profile Model 0165:  [Universal Voltage]

      - Compact design. Cast Aluminum, single-piece construction, with epoxy enamel finish.

      - Brush type electric motor rated 1/4 horsepower.

      - Infrared sensor.

      - Surface mounted with 4-inch projection – ADA Compliant.

      - Finish:  [Grey] or [White].

    - Model 0184: Surface Mounted Sensor Hand Dryer [277 VAC]

      - Steel, single-piece 16-gage drawn steel construction.

      - Brush type electric motor rated 1/4 horsepower, 7500 RPM.

      - Infrared sensor.

      - ADAAG Compliant.

      - Finish: Porcelain Enamel

    - Porcelair Model 0141 [110-120VAC]  [Model 0144, 208-240V]

      - Cast iron housing, single-piece construction, 1/4-inch thick, with acid-resistant porcelain enamel finish.

      - Brushless electric motor rated 1/8 horsepower.

      - Infrared sensor

      - Flip nozzle for face drying

      - Color as selected.

  - HOSPITAL AND MEDICAL SERVICE ACCESSORIES

    - Pass Through Specimen Cabinet:  Model 8154.

      - Self-closing Doors:  22-gage stainless steel, No. 4 satin finish; interlock on doors prevents both doors from being opened at the same time.

      - Cabinet:  22-gage stainless steel, 1-inch flange with 1/4-inch return to wall, four sides; joints welded, sight-exposed welds finished to match sheet finish; adjustable for wall thickness 1-3/4 to 5-1/2 inches.

      - Hinges:  Stainless steel piano hinge, 3/16-inch diameter barrel, full length of cabinet; hinge leaves spot-welded to door and cabinet body.

      - Removable Tray:  22-gage stainless steel.

    - Turntable Specimen Pass Cabinet: Model 0515.

      - Turntable Cylinder Assembly:  18-gage stainless steel, 12-inches diameter, with 10-1/2 by 6 inch opening; removable cylinder housing with lock; No. 4 satin finish.

      - Cabinet Trim:  22-gage stainless steel, 1-inch flange with 1/4-inch returns, four sides; joints welded, sight-exposed welds finished to match sheet finish; adjustable for wall thickness 3 to 7 inches.

      - Main Body:	Self-lubricating ball bearing plate mounted on top and bottom permitting unit to revolve freely; positioned bullet catch prevents uncontrolled rotation.

    - Recessed Bedpan and Urinal Cabinet:  Model 0551.

      - Door:  22-gage stainless steel, with 1/4-inch returns; No. 4 satin finish.

      - Airspace:  1/2-inch, continuous, above and below door.

      - Cabinet:  22-gage stainless steel, 1-inch flange with 1/4-inch return to wall, four sides; joints welded, sight-exposed welds finished to match sheet finish.

      - Hinges:  Stainless steel piano hinge, 3/16-inch diameter barrel, full length of cabinet; hinge leaves spot-welded to door and cabinet body.

    - Foot Operated Surgical Soap Dispenser:  Model 0349.  Pneumatic pump mechanism, 32 ounce (.9 L) polyethylene container. Free turning spout is type 316 stainless steel.

    - Corner Guards:  Model 0533; 18-gage stainless steel, radius corner.  Length as indicated.

- - EXECUTION

  - EXAMINATION

    - Verify openings are sized and located in accordance with shop drawings.

    - Verify reinforcement and anchoring devices are correct type and are located in accordance with shop drawings.

    - Examine conditions under which construction activities are to be performed, then submit written notification if such conditions are unacceptable.

  - INSTALLATION

    - Install accessories in the locations indicated with anchor devices of the types specified.  Fasten securely, true, plumb and level.

      - Install recessed accessories into wall openings with wood screws through cabinet side into wood blocking or studs, or sheet metal screws into metal backing or studs.

      - Install surface mounted accessories to hollow back up using toggle bolts and to metal or wood backing using proper type screws.

      - Provide fasteners, anchors, and the like as necessary to install toilet accessories.

      - Make required electrical connections.

    - Locate toilet accessories at heights specified by ADAAG, State, or local requirements.

  - CLEANING

    - Remove manufacturer's protective coverings and clean surfaces in accordance with manufacturer's recommendations.

  - PROTECTION

    - Protect products from damage caused by subsequent construction activities.

    - Field repair of damaged product finishes is prohibited; replace products having damaged finishes caused by subsequent construction activities.

  - SCHEDULES

    - Commercial Buildings (Class A)

      - Men's Public Washrooms:

        - Mirror at each lavatory except accessible.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*9343 Profile Series Surface Mounted Soap Dispenser / 48 fl oz capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser/Waste Receptacle.

*94696A Profile Series Automatic Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” Wide, 800 ft. Long Rolls / 10-gal. waste receptacle

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser/Seat Cover Dispenser at compartments (back-to-back mounting).

*0484 Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser.

*0485 End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser / ADA Compartment

        - Toilet Tissue Dispenser.

*9030 Profile Series Surface Mounted Dual Roll Toilet Tissue Dispenser [9031 – recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Seat Cover Dispenser at compartment.

*9477SM Profile Series Surface Mounted Seat Cover Dispenser [9477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Baby Changing Station.

*9013 Recessed Stainless Steel Baby Changing Station [9013-9 surface mounted]

        - Hand Dryers.

*0185 Profile Series Surface-Mounted Warm Air Hand Dryer / 185-CFM

*0165 Profile Series Compact Surface-Mounted Warm Air Hand Dryer / 180-CFM

      - Women's Public Washrooms:

        - Mirror at each lavatory except accessible.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*9343 Profile Series Surface Mounted Soap Dispenser / 48 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*94696A Profile Series Automatic Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” Wide, 800 ft. Long Rolls / 10-gal. Waste Receptacle

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser /Seat Cover Dispenser / Napkin Disposal at compartment. *0481 Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal

*0482 End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal / ADA Compartment

        - Toilet Tissue Dispense.

*9030 Profile Series Surface Mounted Dual Roll Toilet Tissue Dispenser [9031 – recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Napkin/Tampon Disposal

*0852 Surface Mounted Sanitary Napkin Disposal

*20470 Roval Recessed Sanitary Napkin Disposal

*20852 Roval Surface Mounted Napkin Disposal

        - Napkin/Tampon Vendor

*94684 Profile Series Recessed Dual Napkin / Tampon Vender – Dispenses 15 Napkins / 23 Tampons

*204684 Roval Recessed Dual Napkin / Tampon Vendor, dispenses 31 napkins and 22 tampons

        - Seat Cover Dispenser at compartment.

*9477SM Profile Series Surface Mounted Seat Cover Dispenser [9477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Baby Changing Station.

*9013 Recessed Stainless Steel Baby Changing Station [9013-9 surface mounted]

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Unisex Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*9343 Profile Series Surface Mounted Soap Dispenser / 48 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*94623 Profile Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste Receptacle

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser.

*9030 Profile Series Surface Mounted Dual Roll Toilet Tissue Dispenser [9031 – recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Napkin / Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

*20470 Roval Recessed Sanitary Napkin Disposal

*20852 Roval Surface Mounted Napkin Disposal

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Seat Cover Dispenser at compartment.

*9477SM Profile Series Surface Mounted Seat Cover Dispenser [9477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Baby Changing Station.

*9013 Recessed Stainless Steel Baby Changing Station [9013-9 surface mounted

      - Men’s Single Toilet Room

        - Mirror at accessible lavatory.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*9343 Profile Series Surface Mounted Soap Dispenser / 48 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*94623 Profile Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste Receptacle

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser.

*9030 Profile Series Surface Mounted Dual Roll Toilet Tissue Dispenser [9031 – recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Seat Cover Dispenser at compartment.

*9477SM Profile Series Surface Mounted Seat Cover Dispenser [9477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

      - Women’s Single Toilet Room

        - Mirror at accessible lavatory.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*9343 Profile Series Surface Mounted Soap Dispenser / 48 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser/Waste Receptacle.

*94623 Profile Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste Receptacle

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser.

*9030 Profile Series Surface Mounted Dual Roll Toilet Tissue Dispenser [9031 – recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Napkin / Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

*20470 Roval Recessed Sanitary Napkin Disposal

*20852 Roval Surface Mounted Napkin Disposal

        - Seat Cover Dispenser at compartment.

*9477SM Profile Series Surface Mounted Seat Cover Dispenser [9477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Janitor's Closet:

        - Utility Shelf/Mop Holder; length 34-inches.

*1308-3 Shelf with Utility Hooks and Mop Strip – 3 Mop Holders / 4 Utility Hooks

    - Heavy Use Commercial Buildings (Convention, Airport, Sports Facilities, Retail)

      - Men's Public Toilet Rooms:

        - Mirror at each lavatory except accessible.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0345 Surface Mounted Soap Dispenser / Horizontal / 40 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle

*04692A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 18-gal. Waste Receptacle

*046921A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 13.3-gal. Waste Receptacle (California Title-24)

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

For Automatics see 2.6.B  Use should be based on volume and function

        - Toilet Tissue Dispenser/Seat Cover Dispenser at compartments (back-to-back mounting).

*0484 Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser

*0485 End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser / ADA Compartment

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Hand Dryers.

*0197-1 (120V) Turbo-Dri Surface Mounted High Speed Automatic Warm Air Hand Dryer [0197-2 (240 VAC)]

*0133 Simplicity Series Recessed Stainless Steel Automatic Warm Air Hand Dryer / 185-CFM

        - Freestanding Waste.

*0829 Corner Waste Receptacle / 15.5 gal. Capacity

      - Women's Public Washrooms:

        - Mirror at each lavatory except accessible.

*0600 Series Angle-Frame Mirror / See sizes on drawings

*20650 Roval Stainless Steel Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0345 Surface Mounted Soap Dispenser / Horizontal / 40 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser/Waste Receptacle.

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle

*04692A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 18-gal. Waste Receptacle

*046921A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 13.3-gal. Waste Receptacle (California Title-24)

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Toilet Tissue Dispenser/Seat Cover Dispenser/Napkin Disposal at compartments (back-to-back mounting). *0481 Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal

*0482 End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal / ADA Compartment

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Napkin/Tampon Disposal at compartment.

*0473-A End Stall Sanitary Disposal Surface Mounted

        - Napkin/Tampon Vendor.

*04684 Traditional Series Recessed Dual Napkin / Tampon Vendor – Dispenses 15 Napkins / 23 Tampons

*204684 Roval Recessed Dual Napkin / Tampon Vendor, dispenses 31 napkins and 22 tampons

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Baby Changing Station.

*9012 Surface Mounted Baby Changing Station / Horizontal {Complies with Accessibility Codes}

        - Hand Dryers.

*0197-1 (120V) Turbo-Dri Surface Mounted High Speed Automatic Warm Air Hand Dryer [0197-2 (240 VAC)]

*0133 Simplicity Series Recessed Stainless Steel Automatic Warm Air Hand Dryer / 185-CFM

        - Freestanding Waste.

*0829 Corner Waste Receptacle / 15.5 gal. Capacity

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Unisex Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0345 Surface Mounted Soap Dispenser / Horizontal / 40 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*0462-AD Traditional Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle

*04692A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 18-gal. Waste Receptacle

*046921A Traditional Series Automatic Roll Paper Towel Dispenser / Waste Receptacle. Dispenses a Pre-set Length from 8” or 9” (205 or 230mm) Wide, 800 ft. (244mm) Long Rolls / 13.3-gal. Waste Receptacle (California Title-24)

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Napkin/Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

*20470 Roval Recessed Sanitary Napkin Disposal

*20852 Revol Surface Mounted Napkin Disposal

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Baby Changing Station.

*9012 Surface Mounted Baby Changing Station / Horizontal {Complies with Handicapped Accessibility Codes}

        - Freestanding Waste.

*0829 Corner Waste Receptacle / 15.5 gal. Capacity

      - Men’s Single Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser / Waste Receptacle.

*0462-AD Traditional Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Toilet Tissue Dispenser.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

      - Women’s Single Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

*20364 Roval Automatic Surface Mounted Soap Dispenser / 33.8 fl oz capacity

*20333 Roval Automatic Deck Mounted Soap Dispenser / 54 fl oz capacity

        - Paper Towel Dispenser/Waste Receptacle.

*0462-AD Traditional Series Paper Towel Dispenser / Waste Receptacle 350 C-fold or 475 Multi-fold Towels / 2-gal. Waste

*204623 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  350 C-fold or 475 multi-fold towels.  3-gal waster receptacle

*20469 Roval Recessed Paper Towel Dispenser / Waste Receptacle.  600 C-fold or 800 multi-fold towels.  14.8-gal waster receptacle

        - Grab Bars as indicated on drawings.

*3801 Series Concealed Mounting Grab Bar 1-1/2” diameter

        - Toilet Tissue Dispenser.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

*20030 Roval Surface Mounted Twin Hide-A-Roll Toilet Tissue Dispenser

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

*20477-SM Roval Surface Mounted Seat Cover Dispenser

        - Napkin/Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

*20470 Roval Recessed Sanitary Napkin Disposal

*20852 Roval Surface Mounted Napkin Disposal

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Janitor's Closet:

        - Utility Shelf/Mop Holder; length 44”.

*1308-4 Shelf with Utility Hooks and Mop Strip - 4 Mop Holders / 5 Utility Hooks

      - Hospital Patient Bathroom:

        - Mirror.

*0620 Series Channel Frame Mirror / See sizes on drawings

        - Soap Dispenser.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser.

*0210 Paper Towel Dispenser 400 C-fold or 525 Multi-fold Towels.

        - Waste Receptacle.

*0828 Waste Receptacle / 6.7 gal. Capacity

        - Toilet Tissue Dispenser.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 - recessed]

        - Cup Dispenser.

*0002-SM Surface Mounted Stainless Steel Paper Cup Dispenser / 100 Flat Bottom Cups 3oz.-6oz.

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” diameter

        - Shower Curtain Rod/ Hooks/ Shower Curtain.

*1214 Heavy-Duty Shower Curtain Rod / *1200-SHU Stainless Steel Shower Curtain Hooks / *1200-V Vinyl Shower Curtain

        - Shower Seat.

*8206 Reversible Folding Shower Seat / Phenolic

        - Robe Hook.

*7382-S Hat and Coat Hook / Satin [7382-B bright]

        - Bed Pan / Urinal Cabinet.

*0551 Recessed Bed Pan and Urinal Cabinet

      - Hospital Exam Room:

        - Waste Receptacle.

*0828 Waste Receptacle / 6.7 gal. Capacity

        - Specimen Pass-Thru.

*8154 Pass Through Specimen Cabinet

        - Double Robe Hook.

*7345-S Double Robe Hook / Satin [7345-B bright]

        - Paper Towel Dispenser (small).

*0215 Paper Towel Dispenser 200 C-fold or 275 Multi-fold Towels.

e.	Soap Dispenser

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

    - Institutional Buildings (Schools, Hospitals, Correctional)

      - School Locker Room:

Check District Paper Contract (Roll Towel vs. Multi-fold)

        - Mirror at each lavatory except accessible.

*0600-B Series Angle Frame Mirror with Tempered Glass / See Sizes on Drawings [0600-L ¼” -Laminated Glass]

        - Mirror at accessible lavatory.

*0535-B Series Fixed Tilt Mirror with Tempered Glass / See Sizes on Drawings [0535-L ¼” Laminated Glass]

        - Soap Dispenser.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Electric Hand Dryer.

*0197-1 (120V) Turbo-Dri Surface Mounted High Speed Automatic Warm Air Hand Dryer [0197-2 (240 VAC)]

        - Toilet Tissue Dispenser at compartments (back-to-back mounting).

*0484 (Men’s) Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser

*0485 (Men’s) End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser / ADA Compartment

*0481 (Women’s) Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal

*0482 (Women’s) End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal / ADA Compartment

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Shower Curtain Rod / Hooks / Shower Curtain.

*1204 Extra Heavy-Duty Shower Curtain Rod / *1200-SHU Stainless Steel Shower Curtain Hooks / *1200-V Vinyl Shower Curtain

        - Heavy Duty Towel Hook.

*8425 Clothes Hook

        - ADA Shower Seat.

*8206 Reversible Folding Shower Seat / Phenolic

      - Men's Public Washrooms:

        - Mirror at each lavatory except accessible.

*0620 Series Channel Frame Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser/Waste Receptacle.

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle

        - Toilet Tissue Dispenser/Seat Cover Dispenser at compartments (back-to-back mounting).

*0484 Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser

*0485 End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser / ADA Compartment

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Electric Hand Dryer.

*0197-1 (120V) Turbo-Dri Surface Mounted High Speed Automatic Warm Air Hand Dryer [0197-2 (240 VAC)

*0133 Simplicity Series Recessed Stainless Steel Automatic Warm Air Hand Dryer / 185 CFM

      - Women's Public Washrooms:

        - Mirror at each lavatory except accessible.

*0620 Series Channel Frame Mirror / See sizes on drawings

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser / Waste Receptacle.

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle.

        - Seat Cover Dispenser at compartment.

*0477-SM Traditional Series Surface Mounted Toilet Seat Cover Dispenser [0477 – recessed]

        - Toilet Tissue Dispenser at compartment.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Toilet Tissue Dispenser/Seat Cover Dispenser/Napkin Disposal at compartment.

*0481 (Women’s) Partition Mounted Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal

*0482 (Women’s) End Stall – Dual Access Seat Cover and Toilet Tissue Dispenser with Sanitary Disposal / ADA Compartment

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Napkin/Tampon Vendor.

*04684 Traditional Series Recessed Dual Napkin / Tampon Vendor – Dispenses 15 Napkins / 23 Tampons

        - Napkin/Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

        - Baby Changing Station.

*9012 Surface Mounted Baby Changing Station / Horizontal {Complies with Handicapped Accessibility Codes}

*9013 Recessed Stainless Steel Baby Changing Station [9013-9 surface mounted]

        - Electric Hand Dryer.

*0197-1 (120V) Turbo-Dri Surface Mounted High Speed Automatic Warm Air Hand Dryer [0197-2 (240 VAC)

*0133 Simplicity Series Recessed Stainless Steel Automatic Warm Air Hand Dryer / 185 CFM

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Unisex Toilet Room

        - Mirror at accessible lavatory.

*0620 Series Channel Frame Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser/Waste Receptacle.

*0469 Traditional Series Paper Towel Dispenser / Waste Receptacle 600 C-fold or 800 Multi-fold Towels / 12-gal. Waste Receptacle

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Toilet Tissue Dispenser recessed.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Baby Changing Station.

*9012 Surface Mounted Baby Changing Station / Horizontal {Complies with Handicapped Accessibility Codes}

*9013 recessed Stainless Steel Baby Changing Station [9013-9 surface mounted]

        - Napkin/Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

        - Electric Hand Dryer.

*0185 Profile Series Surface-Mounted Warm Air Hand Dryer / 185-CFM

      - Men’s Single Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser / Waste Receptacle.

*0462-AD Traditional Series Paper Towel / Waste Receptacle 350 C- Fold or 475 Multi-fold Towels / 2-gal. Waste

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Toilet Tissue Dispenser.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Electric Hand Dryer.

*0185 Profile Series Surface-Mounted Warm Air Hand Dryer / 185-CFM

      - Women’s Single Toilet Room

        - Mirror at accessible lavatory.

*0535 Series Fixed Tilt Mirror / See sizes on drawings

        - Soap Dispenser at lavatory.

*0347 Surface Mounted Soap Dispenser / Vertical / 40 fl Oz Capacity

        - Paper Towel Dispenser/Waste Receptacle.

*0462-AD Traditional Series Paper Towel Dispenser / Waste Receptacle 350 C-fold 0r 475 Multi-fold Towels / 2 gal. Capacity

        - Grab Bars as indicated on drawings.

*3701 Series Concealed Mounting Grab Bar 1-1/4” Diameter

        - Toilet Tissue Dispenser recessed.

*0030 Traditional Series Dual Roll Toilet Tissue Dispenser [0031 – recessed]

        - Napkin/Tampon Disposal.

*0852 Surface Mounted Sanitary Napkin Disposal

        - Folding Utility Shelf.

*0698 Folding Utility Shelf for Toilet Compartment

      - Janitor's Closet:

        - Utility Shelf/Mop Holder; length 34-inches.

*1308-3 Shelf with Utility Hooks and mop Strip – 3 mop Holders / 4 Utility Hooks

      - Inmate Prison Cell:  If accessories rear-mounted, verify wall depths.

        - Metal Mirror.

*107 One Piece Framed Mirror with Rounded Corners / Front Mounting [108 – rear mounting]

        - Soap Dish.

*140 Recessed Soap Dish / Rear Mounting

        - Toilet Tissue Holder

*110-13 Square Recessed Toilet Tissue Holder / Front Mounting [110-1 – rear mounting]

        - Shelf.

*130 Recessed Shelf / Rear Mounting

        - Detention Clothes Hook.

*123 Square Clothes Hook / Front Mounting [122 – rear mounting]

        - Grab Bar.

*164 Grab Bar – 36” / Front Mounting [163 – 36” rear mounting]

        - Grab Bar.

*169 Grab Bar – 48” / Front Mounting [168 – 48” rear mounting]

END OF SECTION