SECTION 10 2813

HAND DRYERS

- - GENERAL

  - SUMMARY

    - Provide electric hand dryers with attachment hardware, rough-in frames, and electrical connection as required for complete, operational installation.

    - Related Requirements

      - See drawings for wall/partition types and additional mounting requirements.

      - Coordinate electrical supply and connection of hand dryers.

      - .	See Section 10 2800 for toilet room accessories.

  - REFERENCES

[Revise to comply with state and local codes for specific project]

    - ADAAG:  Americans with Disabilities Act Accessibility Guidelines.

    - ANSI A117:  Specifications for Making Buildings and Facilities Accessible to and Usable by Physically Handicapped People.

    - IBC – Chapter11, Accessibility.

    - Fair Housing Amendments Act of 1988, Accessibility Guidelines, Federal Register Volume 56, Number 44.

    - State Requirements (i.e., California Building Code Chapter 11)

  - COORDINATION

    - Coordinate locations, dimensions, and other pertinent details with installation of backing, blocking, and electrical connections.

  - LEED® REQUIREMENTS

    - EA Credit 1 – Optimize Energy Performance.

    - MR Credits 1.1 – 1.3 – Sustainable Purchasing:  Ongoing Consumables.

    - MR Credit 4.1 - Recycled Content (post-consumer).

    - MR Credit 4.2 - Recycled Content (post-industrial).

    - MR Credits 7.1 - 7.2 – Solid Waste Management: Ongoing Consumables.

  - SUBMITTALS

    - Submit under provisions of Section 01 3000.

    - Product Data:  Manufacturer's product data for products specified, indicating selected options and accessories.

    - Shop Drawings:

      - Plans:  Locate each specified unit in project.

      - Elevations:  Indicate mounting height of each product.

      - Details:  Indicate anchoring and fastening details, required locations and types of anchors and reinforcement, and materials required for installation of specified products.

    - Verification Samples:  One sample chips of each specified color and finish.

    - Manufacturer's printed installation instructions for each specified product.

    - Closeout Submittals:  Warranty, issued and executed by manufacturer, and countersigned by Contractor.

  - DELIVERY, STORAGE, AND HANDLING

    - Ship products in manufacturer's standard protective packaging with removable protective coating on exposed surfaces.

    - Storage and Protection:  Store products in manufacturer's protective packaging in a dry, climate controlled environment until installation.

  - WARRANTY

    - Provide manufacturer's standard warranty against defects in materials and fabrication.

- - PRODUCTS

  - MANUFACTURERS

    - ASI-American Specialties, Inc.; 441 Saw Mill River Road, Yonkers, NY 10701-4913; Tel:  (914) 476-9000, Fax: (914) 476-0688.  www.americanspecialties.com

    - Furnish products from a single manufacturer.

    - Standard of Quality:  Drawings and specifications are based on proprietary literature from ASI.  Other manufacturers shall comply with the minimum levels of material and detailing indicated on the Drawings and as specified.

  - TURBO-DRI HIGH SPEED HAND DRYER

    - Turbo-Dri.  Model 0197-1, 120V. [0197-2, 240VAC]

      - Cover fabricated of heavy-duty, one piece formed stainless steel 1/16" thick, exposed surfaces satin or bright or heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with white porcelain enamel.

      - Motor:  3/8 - 1 HP, brush type, dual ball bearing, 7000-18000 RPM.

      - Infrared sensor.

      - GreenSpec® listed.

      - Finish:  [Steel housing with Porcelain enamel] or [Stainless steel, {Bright} {Satin} finish].

    - Turbo-Dri optional semi-recessed mounting kit, Model 0119 – ADAAG Compliant.

      - Less than 4-inch protrusion from mounting surface.

  - ROVAL COLLECTION HAND DRYERS

    - Roval Steel Cover, Model 0185 [Universal Voltage]

      - Cover fabricated of heavy-duty, one piece formed stainless steel 1/16" thick, exposed surfaces satin or bright or heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with white porcelain enamel.

      - Motor1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  [Steel housing with Porcelain enamel] or [Stainless steel, {Bright} {Satin} finish].

    - Roval Cast Iron Cover, Model 0195  [Universal Voltage]

      - Cover fabricated of heavy-duty, one piece formed steel 1/16" thick finished on exposed surfaces with porcelain enamel.

      - Motor 1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  Steel housing with Porcelain enamel.

        - Color as selected.

    - Roval Recessed Steel Cover, Model 20199 [120-240 VAC]

      - Cover fabricated of heavy-duty, one piece formed 18-gage stainless steel exposed surfaces.

      - Motor 0.69 HP, brush type, dual ball bearing, 29000 RPM.

      - Infrared sensor.

      - Finish:  Stainless steel, Satin finish.

  - SIMPLICITY COLLECTION HAND DRYERS

    - Model 0133  [Universal Voltage]

      - Cover fabricated of heavy-duty, 14-gage seamless stainless steel cover, exposed surfaces satin finish.

      - Motor:  1/4 HP, brush type, dual ball bearing, 7500 RPM.

      - Infrared sensor.

      - Finish:  Stainless steel, Satin finish.

    - Model 64673, Three-in-one unit recessed combination paper towel dispenser, automatic hand dryer and waste receptacle.

      - Three-in-one unit combines towel dispenser, automatic hand dryer and a four gallon stainless steel waste receptacle in one unit.

  - PROFILE COLLECTION HAND DRYERS

    - Profile Model 0165:  [Universal Voltage]

      - Compact design. Cast Aluminum, single-piece construction, with epoxy enamel finish.

      - Brush type electric motor rated 1/4 horsepower.

      - Infrared sensor.

      - Surface mounted with 4-inch projection – ADA Compliant.

      - Finish:  [Grey] or [White].

    - Model 0184: Surface Mounted Sensor Hand Dryer [277 VAC]

      - Steel, single-piece 16-gage drawn steel construction.

      - Brush type electric motor rated 1/4 horsepower, 7500 RPM.

      - Infrared sensor.

      - ADAAG Compliant.

      - Finish: Porcelain Enamel

  - PORCELAIR HAND DRYERS

    - Porcelair Model 0141 [110-120VAC]  [Model 0144, 208-240VAC]

      - Cast iron housing, single-piece construction, 1/4-inch thick, with acid-resistant porcelain enamel finish.

      - Brushless electric motor rated 1/8 horsepower.

      - Infrared sensor

      - Flip nozzle for face drying

      - Color as selected.

- - EXECUTION

  - EXAMINATION

    - Verify openings are sized and located in accordance with shop drawings.

    - Verify reinforcement and anchoring devices are correct type and are located in accordance with shop drawings.

    - Examine conditions under which construction activities are to be performed, then submit written notification if such conditions are unacceptable.

  - INSTALLATION

    - Install hand dryers in the locations indicated with anchor devices of the types specified.  Fasten securely, true, plumb and level.

      - Install recessed hand dryers into wall openings with wood screws through cabinet side into wood blocking or studs, or sheet metal screws into metal backing or studs.

      - Install surface mounted accessories to hollow back up using toggle bolts and to metal or wood backing using proper type screws.

      - Provide fasteners, anchors, and the like as necessary to install toilet accessories.

      - Make required electrical connections.

    - Locate hand dryers at heights specified by ADAAG, State, or local requirements.

  - CLEANING

    - Remove manufacturer's protective coverings and clean surfaces in accordance with manufacturer's recommendations.

  - PROTECTION

    - Protect products from damage caused by subsequent construction activities.

    - Field repair of damaged product finishes is prohibited; replace products having damaged finishes caused by subsequent construction activities.

END OF SECTION